## Slide 2
Quality Control Presentation
October 2020
All Natural Product

## Slide 3: NOTICE OF CONFIDENCIALITY This presentation has been produced by Krustagroup S.A.U. solely in the interest and on request of COSTCO. COSTCO undertakes to keep the contents of this presentation (“Confidential Information”) strictly confidential. Consequently, the following COSTCO’s obligations of secrecy, non-disclosure and non-use shall apply: 1. Not to disclose, publish or disseminate, directly or indirectly, the Confidential Information in any way to anyone and COSTCO agrees to take reasonable precautions to prevent any unauthorized use, disclosure, publication or dissemination of Confidential Information; 2. Not use the Confidential Information for any purpose; 3. Not improperly make use of the Confidential Information for its own benefit, or that of any third party, or use such Confidential Information to the detriment of Krustagroup or any third party.

## Slide 4: THE CHALLENGE STARTED IN 2018 WITH THIS SITUATION
Argentine Shrimp land frozen fishing industry particularities
It´s a wild catch.
Fishing and processing is divided into many small independent companies.
Depending on the period of the year, different fishing areas and production sites are suitable.
General lack of liquidity affecting to processors does not allow to wait for customer needs.

## Slide 5: THE OPPORTUNITIIES STARTED IN 2018
We created a new category of shrimp wild catch
We produce single frozen free chemical product.
We have the best possible partner for our production plan in Puerto Madryn, fully commited with this Project.
Investment plan already approved to have three factories (one exclusively dedicated Free Chemical processing) and improved coldstorage capacity.
We work all year through, fishing during Province and National Campaigns (11 months).
We control temperature during all the process.
So we create a consistent supply program of Argentine Red Shrimp to the US Market, in terms of quality, product adaptation and fulfilment of commitments.

## Slide 6: THE ONLY ALL NATURAL OPERATION IN ARGENTINA

## Slide 7
Chart: 
| 2018 | 2019 | 2020 | 2021
loads | 1 | 21 | 74 | 120
Loading plan since 2018

## Slide 8
Technical Aspects
1.Quality control on board
2. Temperature limits
After the technical analysis of last fishing campaigns in National and Province Waters, we present our proposal to develop Kirkland Signature (KS) Campaign 2020/2021 and comply with sheduled production plan

## Slide 9
This is not mandatory nor a requirement for the Argentine Sanitary Authorities. The fresh fleet does not process the raw material on the vessel.
The Argentine vessels are under sanitary registries of SENASA: GMP (Good Manufacturing Practises), National & Province Campaign Secretary of Fishery.
1. Quality control on board

## Slide 10
The quality inspector on board is not a mandatory requirement for fishing vessels.
We accepted this request when starting our relationship with Costco but it´s impossible to do it with the dimension gained, more than 100 loads planned for Campaign 2020/2021.
National regulatory authority has the power to assign observers on board with special permits during the exploration stages.
On the artisanal fleet (Province Campaign) there is no space for an external observer. Average maximum number of crew 4 people. Catch time is less than 15 hours.
The organoleptic characteristics of the raw material are optimal. There is no history of deviations that require the incorporation of a quality inspector on board. It would replace the position of a seaman.
1.1. Why is it not necessary?

## Slide 11
1.2. Some regulations from SENASA talking about that
Unloading control procedure of the fresh vessels
1) When a vessel arrives at port, Senasa staff will request a photocopy of the Fishing Report, authorize the unloading and carry out routine organoleptic controls. He will then intervene the remittances that will accompany the cargo in its respective transport for its subsequent validation.
2) The referred validation will consist of registering in the Fishing Report, the species transported and its destination. In places where there is no validation office, this will be carried out at the destination plants, either for processing or for release in order to process in another establishment.
3) The validation will be carried out over the total of the merchandise landed; This will allow knowing the destination of the same, either in the establishments authorized by Senasa or in those that have only municipal and / or provincial authorization, thus completing the control over the movement of fish in general.
4) Senasa personnel will prepare a pre-operative form prior to the departure of the ship. This form will be used
by the shipowners and / or whoever is responsible for the ship so that these vessels are adapted to current regulations.
http://www.senasa.gob.ar/normativas/resolucion-348-2007-senasa-servicio-nacional-de-sanidad-y-calidad-agroalimentaria

## Slide 12
How we decrease temperatura since catching to process final steps
Target: to reach less than 10ºC after catching and to keep it below 5ºC during the manufacturing
2º TERMICAL SHOCK AT PORT
. RE-ICING IN TRUCKS
. 1/5 TO 1/3 ICE/SHRIMP
Thermal Shock: we are the only company that performs this action. We will continue to guarantee ice conservation, boxes and optimal transport during all campaigns.
2. Temperature limits (Province Campaign)
TRIP TO FISHING GROUND | FROM 1º CATCHING TO COME BACK TO PORT | UNLOADING AND TRANSPORT TO MADRYN | TERMICAL SHOCK AND START PRODUCTION
 | 0-15H | 2-3H | FOODPARTNERS

## Slide 13: Data and analysis of product captured
1. Sea temperature:
The temperature of the product will fluctuate according to the temperature of the natural habitat (sea)

## Slide 14
2. Products on board :
3. In hold on board (product) – 1st thermal shock

## Slide 15
3. Conditioning on deck/ Discharge on deck :
See attached video of the 2nd thermal shock in transport.
A- Ship Unloading
See attached video of the 2nd thermal shock in transport.
B- Loading truck :

## Slide 16
4. Reception of raw material (land plant)
If needed, product will be reconditioned with ice and kept in a cool chamber while waiting for processing.
Acceptance/refusal or corrective measures are applied. The organoleptic values ​​should be optimal. Temperature is not a quality condition. It is only a variable that is controlled throughout the process.

## Slide 17: Let's talk about temperatures and organoleptic values HACCP / SENASA / FDA
Our factory never experienced a case of development of pathogens due to loss of cold. Our recommendation is to use 10ºC as a limit (maximum) and corrective action as defined at the free chemical product spech sheet.
  Corrective action: when it appears go over and refill with ice, send directly to the cold room keeping the temperature at an average of 5ºC
FDA:
  Chapter 12- Fish & Fishery products hazards and control. Page 211. defines that bacterial growth is very slow below 10ºC

## Slide 18
GMP (Good Manufacturing Practices)
Temperature is a variable that can modify the quality of the product, therefore, temperature as a single value, is not a determining factor of the quality or acceptance of the product.
ONE OF THE MOST IMPORTANT REASONS is that we use temperature control to control
the development of pathogens; as indicated by the Haccp of Food Partners, in its hazard analysis.
During all the processes the organoleptic characteristics of the product, temperatures, calibers, glazing, defects are controlled according to the requirement of the product and the quality management system.
In the event of any deviation, the measures indicated in the Haccp will be applied.
HACCP/ SENASA /FDA

## Slide 19
Temperature / Process

## Slide 20
Process /Temperature /Time

## Slide 21: During the process, water-ice thermal shocks will be applied, and the organoleptic values ​​will be observed. Senasa / HACCP requirements; the product will be removed in case of alterations.
5. Raw material storage chamber (fresh):
6. Processing:

## Slide 22
7. De-head, manually or mechanically wash:
In this headless process, the raw material is washed and conditioned with ice and waiting to be peeled and deveined.

## Slide 23
8. Size: Grade and inspect
During this process, the pieces are peeled and classified, washed with ice water. There is a quality control of defects, size, temperature. This whole process is kept below 5ºC (water-ice thermal)

## Slide 24
9. Freeze/Glaze:
During this process % glaze, % defects, freezing temperatures and other items are verified.
Organoleptic values continue to be verified. GLAZE: 8% -12% consistent glaze that surrounds entire shrimp

## Slide 25
10. Pack in plastic bag/ Metal Detection/ Pack in master carton:
During this process: glaze, net weights, gross weights and defects are verified. Deficient pieces are discarded. Control of % defects, pieces per bag. Traceability of bags, cases among others.

## Slide 26
11. Pack in plastic bag/ Metal Detection/ Pack in master carton:
Deficient pieces are discarded

## Slide 27
11.1. Pack in plastic bag/ Metal Detection/ Pack in master carton:

## Slide 28
12. Frozen Storage – Ship:

## Slide 29
13. We verify the quality during all the processes
The controls are designed according to the technical specification of the product and / or customer requirement.
We adapt the production processes to the customer necessities
We conform to the pre-audited producer's Haccp
We do pre-audit of the vessels to verify that they comply with the quality regulation approved

## Slide 30
Examples of our Quality Controls
DETALLE DE CARGAS PIER 33 - KRUSTAGROUP / PATAGONIA SHIRMP |  |  |  |  |  |  |  |  |  |  | 
Nº CARGA | DIA DE CARGA | FRIGORIFICO Nº 4055 | MARCA | CAMPAÑA | Nº OPERACIÓN | DESTINO | REMITO Nº | PND 10-30 (BOX ) | PND 30-50 (BOX) | PIER QC EXCEL | CONTROL PACKAGING
24 | 08/07/2020 | F. PARTNERS | PIER33 | NACION | 1136 | LONG BEACH- LA | 1417 | 1350 | 0 | OP1136 QC PIER33 | LNXU 755 586-5
25 | 08/07/2020 | F. PARTNERS | PIER33 | NACION | 1140 | LONG BEACH- LA | 1419 | 1350 | 0 | OP1140 QC PIER33 | TCLU 118 048-2
Pier 33 by GrandKrust Argentine Red Shrimp Inspection Report |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PO Number: |  |  |  |  |  |  |  |  |  |  | Lot Number: |  | 4055 8620182 |  |  | 
Inspection Date: | 01/07/2020 - 03/07/2020 - 05-07-2020 |  | Supplier Name (Tier 1): |  | Camanchaca Inc |  |  | Origin: | Argentina |  | Product Status: |  |  |  |  | 
Inspected by: |  |  | Packer (Tier 2): |  | FOOD PARTNERS PATAGONIA S.A. |  |  | Pack Size: | 14 x 680 g |  | Retention Date: |  |  |  |  | 
PC/Description: | 10-30 All-Natural Argentine Red Shrimp |  | FDA# |  |  |  |  | Cases: |  |  | Short Weight (oz.): |  |  |  |  | 
Brand: | Pier 33 Gourmet |  | SENASA # |  |  |  |  |  |  |  |  |  |  |  |  | 
NOTE: SAMPLING SIZE = Sample Size – 3 Bags -- Finished Product Samples will be evaluated in a thawed state – per lot |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Comments: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Plant Production & Sample Information |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Sample No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | Average | NOTES:
 | Spec. |  |  |  |  |  |  |  |  |  |  |  |  |  | - | 
Production Date | - | 30/06/2020 | 30/06/2020 | 30/06/2020 | 30/06/2020 | 30/06/2020 | 30/06/2020 | 30/06/2020 | 30/06/2020 | 30/06/2020 |  |  |  |  | - | 
Lot Traceable | - | 4055 8620182 | 4055 8620182 | 4055 8620182 | 4055 8620182 | 4055 8620182 | 4055 8620182 | 4055 8620182 | 4055 8620182 | 4055 8620182 |  |  |  |  | - | 
 |  | GRAMS |  |  |  |  |  |  |  |  |  |  |  |  | - | 
Gross Weight with Bag (g) | 787 g | 792 | 796 | 796 | 794 | 789 | 792 | 797 | 794 | 792 |  |  |  |  | 793,56 | 
Tare Weight Bag (g) | 19 g | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 |  |  |  |  | 19,00 | 
Sub Sample Net Wt. (g) | 768 g | 773 | 777 | 777 | 775 | 770 | 773 | 778 | 775 | 773 |  |  |  |  | 774,56 | 
Net Wt. (g) - Following AOAC Int't Standard for deglazing | 680g | 701 | 700 | 701 | 700 | 700 | 696 | 703 | 696 | 698 |  |  |  |  | 699,44 | 
Units Per Bag | 15 - 45 | 40 | 40 | 40 | 41 | 39 | 38 | 41 | 40 | 40 |  |  |  |  | 40 | 
Black Spots (on Meat) (g) | < 10% by weight | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  | - | 
Dehydration (g) | NONE | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  | - | 
Decompositon (g) | NONE | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  | - | 
Foreign Material (g) | NONE | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  | - | 
Shells, Legs, Swimmerettes - Attach Pictures (g) | < 1% by weight | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  | - | 
Imporperly Deveined (g) - Attach Pictures | < 2% by weight | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  | - | 
Broken and Pieces (g) (< 4 segments) - Attach Pictures | < 7% by weight | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  | - | 
Neck Meat (g) | Shall not be longer than first segment or discolored (yellow / brown) or dirty ( < 10% by weight) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  | - | 

## Slide 31
¡Thank You !